## Slide 1
Four local GINE actors choose topology actions; one global critic guides MAPPO
Current WCCI-36 configuration · decentralized execution · centralized training
DECENTRALIZED ACTOR πᵢ
× 4 agents · same architecture · weights not shared
Local busbar graph Gᵢ
Nodes: local busbars
Edges: feasible line connections
Topology: active-edge mask
Node tensor
6 physical features
+ 8-D substation ID
+ 8-D busbar ID
22 features / node
Edge tensor
6 line features
status · ρ · overload
cooldown · maintenance
GINE graph encoder
Node MLP: 22 → 64
ReLU · LayerNorm
1 edge-aware message-passing layer
hidden dimension: 64
Graph readout
Mean pooling
over local nodes
Linear 64 → 64 · ReLU
Actor MLP
64 → 128 → 128
ReLU activations
Categorical policy
128 → Kᵢ action logits
train: sample aᵢ
eval: argmax aᵢ
nᵢ = 2 × controlled substations
CENTRALIZED TRAINING
Joint flat observation
[o₀ ∥ o₁ ∥ o₂ ∥ o₃]
77 + 150 + 139 + 377
= 743 features
Centralized critic
MLP 743 → 128 → 128 → 1
ReLU activations
State value V(s)
Single scalar estimate
MAPPO update
GAE advantages + returns
Clipped policy loss
Entropy bonus + value loss
WCCI-36 environment
Joint action (a₀…a₃)
AC power flow
reward · next state
policy gradients
value gradients

## Slide 2
A fixed chronic split separates policy learning from model selection
Agents act every five simulated minutes; held-out chronics never enter MAPPO training
TOPOLOGY ACTION SPACE
Each agent selects one local action
The four agents’ selections are combined into one joint grid-control decision.
0
Do nothing
Preserve the current topology
↔
Switch a transmission line
Connect or disconnect a line
1|2
Reassign substation elements
Move components between busbars
Every 5 minutes · shared grid-level reward
CHRONIC SPLIT & EVALUATION
Available chronics
fixed shuffle · split seed 0
LEARNING
MODEL SELECTION
80% training chronics
Only these chronics generate policy updates
MAPPO rollouts & updates
72 parallel environments in the current WCCI runs
Train-split evaluation
Diagnostic only · does not choose the checkpoint
20% held-out test chronics
Never used for gradient updates
Deterministic test evaluation
Greedy actions on a held-out subset during training
Best checkpoint
Selected by mean held-out test survival
Final full-split evaluation
Every chronic in the complete held-out test split

## Slide 3
The IEEE-14 reference baseline trains for 25M steps with 80 PPO epochs
Original MAPPO hyperparameters reproduced before architectural changes
Hyperparameter | Value
TRAINING | 
Total timesteps | 25M
Rollout steps per environment | 2,000
Total rollout batch | 20,000
Evaluation frequency | 80,000
NETWORK | 
Actor architecture | MLP · 256 × 3
Critic architecture | MLP · 256 × 3
Activation | ReLU
Hyperparameter | Value
PPO OPTIMIZATION | 
Actor learning rate | 3 × 10⁻⁵
Critic learning rate | 3 × 10⁻⁵
Learning-rate schedule | Linear decay
Discount factor γ | 0.99
GAE parameter λ | 0.95
Update epochs | 80
Minibatches | 4
Clip coefficient ε | 0.20
Target KL | 0.02
Maximum gradient norm | 10.0
Entropy coefficient | 0.01
Value-loss coefficient | 0.50
Source: original IEEE-14 MAPPO baseline hyperparameters