## Slide 1
Four local GINE actors choose topology actions; one global critic guides MAPPO
Current WCCI-36 configuration · decentralized execution · centralized training
DECENTRALIZED ACTOR πᵢ
Local busbar graph Gᵢ
Nodes: local busbars
Edges: feasible line connections
Topology: active-edge mask
Node tensor
6 physical features
+ 8-D substation ID
+ 8-D busbar ID
22 features / node
Edge tensor
6 line features
status · ρ · overload
cooldown · maintenance
GINE graph encoder
Node MLP: 22 → 64
ReLU · LayerNorm
1 edge-aware message-passing layer
hidden dimension: 64
Graph readout
Mean pooling
over local nodes
Linear 64 → 64 · ReLU
Actor MLP
64 → 128 → 128
ReLU activations
Categorical policy
128 → Kᵢ action logits
train: sample aᵢ
eval: argmax aᵢ
nᵢ = 2 × controlled substations
CENTRALIZED TRAINING
Joint flat observation
[o₀ ∥ o₁ ∥ o₂ ∥ o₃]
77 + 150 + 139 + 377
= 743 features
Centralized critic
MLP 743 → 128 → 128 → 1
ReLU activations
State value V(s)
Single scalar estimate
MAPPO update
GAE advantages + returns
Clipped policy loss
Entropy bonus + value loss
WCCI-36 environment
Joint action (a₀…a₃)
AC power flow
reward · next state
policy gradients
value gradients

## Slide 2
Four local GINE actors choose topology actions; one global critic guides MAPPO
Current WCCI-36 configuration · decentralized execution · centralized training
DECENTRALIZED ACTOR πᵢ
Local busbar graph Gᵢ
Nodes: local busbars
Edges: feasible line connections
Topology: active-edge mask
Node tensor
6 physical features
+ 8-D substation ID
+ 8-D busbar ID
22 features / node
Edge tensor
status · ρ · overload
cooldown · (maintenance if present)
GINE graph encoder
Node MLP: 22 → 64
ReLU · LayerNorm
2 edge-aware message-passing layer
hidden dimension: 64
Graph readout
Mean pooling
over local nodes
Linear 64 → 64 · ReLU
Actor MLP
64 → 128 → 128
ReLU activations
Categorical policy
128 → Kᵢ action logits
train: sample aᵢ
eval: argmax aᵢ
CENTRALIZED TRAINING
Joint flat observation
[o₀ ∥ o₁ ∥ o₂ ∥ o₃] size n_o
Centralized critic
MLP n_o → 128 → 128 → 1
ReLU activations
State value V(s)
Single scalar estimate
MAPPO update
GAE advantages + returns
Clipped policy loss
Entropy bonus + value loss
WCCI-36 environment
Joint action (a₀…a₃)
AC power flow
reward · next state

## Slide 3
A fixed chronic split separates policy learning from model selection
Agents act every five simulated minutes; held-out chronics never enter MAPPO training
TOPOLOGY ACTION SPACE
Each agent selects one local action
The four agents’ selections are combined into one joint grid-control decision.
0
Do nothing
Preserve the current topology
↔
Switch a transmission line
Connect or disconnect a line
1|2
Reassign substation elements
Move components between busbars
Every 5 minutes · shared grid-level reward
CHRONIC SPLIT & EVALUATION
Available chronics
fixed shuffle · split seed 0
LEARNING
MODEL TESTING
80% training chronics
Only these chronics generate policy updates
MAPPO rollouts & updates
72 or 20 parallel environments
Train-split evaluation
Diagnostic of the training
20% held-out test chronics
Never used for gradient updates
Deterministic test evaluation
Greedy actions on a held-out subset during training
Best checkpoint
Selected by mean held-out test survival
Final full-split evaluation
Every chronic in the complete held-out test split
Best checkpoint
Selected by mean held-out test survival

## Slide 4
A fixed chronic split separates policy learning from model selection
Agents act every five simulated minutes; held-out chronics never enter MAPPO training
TOPOLOGY ACTION SPACE
Each agent selects one local action
The four agents’ selections are combined into one joint grid-control decision.
Every 5 minutes · shared grid-level reward
CHRONIC SPLIT & EVALUATION
Available chronics
fixed shuffle · split seed 0
LEARNING
MODEL TESTING
80% training chronics
Only these chronics generate policy updates
MAPPO rollouts & updates
72 or 20 parallel environments
Train-split evaluation
Diagnostic of the training
20% held-out test chronics
Never used for gradient updates
Deterministic test evaluation
Greedy actions on a held-out subset during training
Final full-split evaluation
Every chronic in the complete held-out test split
Best checkpoint
Selected by mean held-out train survival
Do nothing
  Preserve the current topology
Switch a transmission line
  Connect or disconnect a line
Reassign a substation elements
  Move components between busbars

## Slide 5
The IEEE-14 reference baseline trains for 25M steps with 80 PPO epochs
Original MAPPO hyperparameters reproduced before architectural changes
Hyperparameter | Value
TRAINING | 
Total timesteps | 25M
Rollout steps per environment | 2,000
Total rollout batch | 20,000
Evaluation frequency | 80,000
NETWORK | 
Actor architecture | MLP · 256 × 3
Critic architecture | MLP · 256 × 3
Activation | ReLU
Hyperparameter | Value
PPO OPTIMIZATION | 
Actor learning rate | 3 × 10⁻⁵
Critic learning rate | 3 × 10⁻⁵
Learning-rate schedule | Linear decay
Discount factor γ | 0.99
GAE parameter λ | 0.95
Update epochs | 80
Minibatches | 4
Clip coefficient ε | 0.20
Target KL | 0.02
Maximum gradient norm | 10.0
Entropy coefficient | 0.01
Value-loss coefficient | 0.50
Source: original IEEE-14 MAPPO baseline hyperparameters

## Slide 6
The graph encoder maps injections to nodes and line conditions to edges
WCCI-36 adds maintenance information on edges; redispatch and curtailment stay outside the core graph
Feature category | Observation variables | Graph role
Generation | gen_p, gen_theta | Node
Demand | load_p, load_theta | Node
Line loading | rho | Edge
Line status | line_status | Edge + active mask
Overload duration | timestep_overflow | Edge
Line cooldown | time_before_cooldown_line | Edge
Substation cooldown | time_before_cooldown_sub | Node
Topology | topo_vect | Busbar nodes + edge mask
Maintenance forecast | time_next_maintenance, duration_next_maintenance | Edge · WCCI-36 only
Redispatch state | target_dispatch, actual_dispatch, gen_margin_up/down | Outside core graph
Curtailment state | gen_p_before_curtail, curtailment, curtailment_limit | Outside core graph
Controlled region | Agent's assigned substations | Node · domain_mask
Source: observation schema implemented in GridGraphBuilder

## Slide 7
Topology-control research is moving toward coordinated regional agents
Representative Grid2Op / L2RPN studies · references [1]–[6]
SINGLE AGENT
One policy sees the grid and chooses from a global action set
MULTI-AGENT
Control is divided by substation or region, then coordinated
2021
Simple deep RL baseline [1]
IEEE-14 topology switching; strong transfer from one training scenario.
2021
Hierarchical SMAAC [2]
Graph attention + afterstate evaluation reduce the global decision burden.
2021
Policy-guided safe search [3]
The policy proposes candidates; Grid2Op simulation filters unsafe actions.
2023
Substation-level MARL [4]
Independent / dependent PPO and SACD agents are tested in a hierarchy.
2025
Centrally coordinated MARL [5]
Regional agents propose actions; a learned or greedy coordinator selects one.
2026
MARL2Grid-TR benchmark [6]
Configurable local observability and agents for topology and redispatch control.
OPEN CHALLENGE
Stable coordination on large grids under partial observability and safety constraints remains unresolved.

## Slide 8
References
Representative Grid2Op / L2RPN topology-control literature cited in the review
1
Subramanian, M., Viebahn, J., Tindemans, S. H., Donnot, B., & Marot, A. (2021). Exploring grid topology reconfiguration using a simple deep reinforcement learning approach. IEEE Madrid PowerTech.
doi.org/10.1109/PowerTech46648.2021.9494879
2
Yoon, D., Hong, S., Lee, B.-J., & Kim, K.-E. (2021). Winning the L2RPN Challenge: Power grid management via semi-Markov afterstate actor-critic. ICLR 2021.
openreview.net/forum?id=LmUJqB1Cz8
3
Zhou, B., Zeng, H., Liu, Y., Li, K., Wang, F., & Tian, H. (2021). Action set based policy optimization for safe power grid management. ECML PKDD 2021.
arxiv.org/abs/2106.15200
4
van der Sar, E., Zocca, A., & Bhulai, S. (2023). Multi-agent reinforcement learning for power grid topology optimization. arXiv:2310.02605.
arxiv.org/abs/2310.02605
5
de Mol, B., Barbieri, D., Viebahn, J., & Grossi, D. (2025). Centrally coordinated multi-agent reinforcement learning for power grid topology control. arXiv:2502.08681.
arxiv.org/abs/2502.08681
6
Marchesini, E., Boguslawski, E., Leite, A., Amato, C., Dussartre, M., Schoenauer, M., Donnot, B., & Donti, P. L. (2026). MARL2Grid-TR: A multi-agent RL benchmark in power grid operations. ICLR 2026.
openreview.net/forum?id=mpAMH1OyMO